; READ TASTE PINA(0)
; READ DATA(3:0) = PINA(4:7)
; PINA(0) = 1: pass thru PORTC(3:0) = PINA(4:7)
; PINA(0) = 0: PORTC(2:0) = INVERT PINA(4:7)
; used pins of A: PINA(0) taste, PINA(4:7) DATA, rest: PINA(3:1) = WRITE PINS for extension
; all PINS of PORTC are write pins

.DEF ACC1 = R16; use acc1 instead of R16
.DEF ACC2 = R17; use acc2 instead of R17
.DEF HELP = R18;

.EQU takt = 16000000;

.CSEG
rjmp start;
.ORG 0x40; do not write code into interrupt table, start write code at 16 bit address 0x40, (outside interrupt table

start:

    ; initialize stack pointer at indirect ram address
; SP is the pointer to indirect addressable ram
ldi ACC1, LOW(RAMEND);
out SPL, ACC1;
ldi ACC1, HIGH(RAMEND);
out SPH, ACC1;

; initalize portA A(7:0) R R R R W W W R
ldi ACC1, 0b00001110;
out DDRA, ACC1;

ldi ACC1, 0xFF;
out DDRC, ACC1;

; main programm
loop: ; forever
call read_taste; read PINA(0) -> ACC1
call read_data; read PINA(7:4) -> ACC2
call write_data; DATA(3:0) -> PORTC(3:0) taste = 1, write invert DATA(3:0) -> taste = 0

rjmp loop;

read_taste:
in ACC1, PINA;
ANDI ACC1, 0b00000001; clear bits(7:1) keep bit0 untouched
ret;

read_data:
in ACC2, PINA;
ANDI ACC2, 0b11110000; mask data clear bits(3:0)
; shift AAC1(7:4) --> ACC1(3:0)
lsr ACC2;
lsr ACC2;
lsr ACC2;
lsr ACC2;

ret;

write_data:

   ; is taste pressed?
   ldi HELP, 0x01;
cp ACC1, HELP; set zero bit if HELP == 0x01

; jump if zero bit is set
breq path_thru; pass data to PORT C

invert:
; we can use acc1 again, we use acc1 at next loop
ldi ACC1, 0b00001111; invert lower four bits
EOR ACC2, ACC1;
out PORTC, ACC2; write the bits
        ret;

path_thru:
out PORTC, ACC2; write the bits

ret;

write_7SEG: